## Slide 1
Preliminary Study on
Green Infrastructure Monitoring data

## Slide 2
Bioswale
Bioswales are channels designed to concentrate and convey stormwater runoff while removing debris and pollution. Bioswales can also be beneficial in recharging groundwater.
%VWC
Volumetric water content is a numerical measure of soil moisture. It is simply the ratio of water volume to soil volume. Another equally valid measurement is GWC, gravimetric water content, which measures weight rather than volume.

## Slide 3
What do we have
CSV file of 3.34gb
CSV migrated to AWS S3 standard – US East (North Virginia) Region.
After Moving to S3 3.34 was converted to 3.43GB
AWS IAM user was created to create access for S3
S3 Bucket access to DataBricks by mounting
Data Frame & Schema
We have a total of 1,32,99,699 observations, 16 features.
While reading data from AWS schema was inferred automatically

## Slide 4
Measurement Title
UI lab, Langley, Argyle
13 station units each aggregating to 39 station units
Each cell – One Attribute
MK-III stations are long range stations with 2.4GHz frequency.
Data Overview
Measurement Title | Company Name
UI Labs Bioswale - Thunder 1: MK-III Weather Station Wind Direction | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station Wind Direction | Langley
Argyle - Thunder 1: MK-III Weather Station Wind Direction | Argyle
UI Labs Bioswale - Thunder 1: MK-III Weather Station RH | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station RH | Langley
Argyle - Thunder 1: MK-III Weather Station RH | Argyle
UI Labs Bioswale - Thunder 1: MK-III Weather Station Pressure | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station Pressure | Langley
Argyle - Thunder 1: MK-III Weather Station Pressure | Argyle
UI Labs Bioswale - Cumulus: Weather Station Pressure | UI Labs Bioswale
Langley - Cumulus: Weather Station Pressure | Langley
Argyle - Cumulus: Weather Station Pressure | Argyle
UI Labs Bioswale - Thunder 1: MK-III Weather Station Wind Speed | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station Wind Speed | Langley
Argyle - Thunder 1: MK-III Weather Station Wind Speed | Argyle
UI Labs Bioswale - Cumulus: Weather Station Wind Speed | UI Labs Bioswale
Langley - Cumulus: Weather Station Wind Speed | Langley
Argyle - Cumulus: Weather Station Wind Speed | Argyle
UI Labs Bioswale - Thunder 1: MK-III Weather Station Temp | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station Temp | Langley
Argyle - Thunder 1: MK-III Weather Station Temp | Argyle
UI Labs Bioswale - Cumulus: Weather Station Air Temp | UI Labs Bioswale
Langley - Cumulus: Weather Station Air Temp | Langley
Argyle - Cumulus: Weather Station Air Temp | Argyle
UI Labs Bioswale - Thunder 1: MK-III Weather Station Rainfall | UI Labs Bioswale
Langley - Thunder 1: MK-III Weather Station Rainfall | Langley
Argyle - Thunder 1: MK-III Weather Station Rainfall | Argyle
Langley - Cumulus: Weather Station Rainfall | Langley
Argyle - Cumulus: Weather Station Rainfall | Argyle
UI Labs Bioswale - Thunder 1: TM1 Temp Sensor | UI Labs Bioswale
Langley - Thunder 1: TM1 Temp Sensor | Langley
Argyle - Thunder 1: TM1 Temp Sensor | Argyle
UI Labs Bioswale - Thunder 1: SM1 Soil Moisture Sensor | UI Labs Bioswale
Langley - Thunder 1: SM1 Soil Moisture Sensor | Langley
Argyle - Thunder 1: SM1 Soil Moisture Sensor | Argyle
UI Labs Bioswale NWS Quantitative Precipitation Forecast | UI Labs Bioswale
UI Labs Bioswale NWS Probability of Precipitation | UI Labs Bioswale
Langley - Cumulus: Bioswale Calibrated VWC | Langley
Argyle - Cumulus: Bioswale Calibrated VWC | Argyle

## Slide 5
Location
Company | Latitude | Longitude | Address
UI Labs Bioswale | 41.9072 | -87.6540 | 1333 North Hickory Avenue, Chicago, IL 60642, Near North Side Chicago Illinois United States
Langley | 41.7531 | -87.6077 | 7750 South Langley Avenue, Chicago, IL 60619, Greater Grand Crossing Chicago Illinois United States
Argyle | 41.9731 | -87.6597 | 5012 North Broadway, Chicago, IL 60640, Uptown Chicago Illinois United States
 | Min (kms) | Max (Kms)
UI <-> Langley | 20.1 | 24.1
UI <-> Argyle | 9.9 | 12.3
Langley <-> Argyle | 30 | 32

## Slide 6
Measurement Description
Data Overview
Type of Station (MK-III, Cumulus, Sensor)
Nulls when description is not either Mk-III or Sensor
Measurement_Description
MK-III Weather Station Wind Direction
MK-III Weather Station RH
MK-III Weather Station Pressure
Nulls (Pressure)
MK-III Weather Station Wind Speed
Nulls (WindSpeed)
MK-III Weather Station Temp
Nulls (Temp)
MK-III Weather Station Rainfall
Nulls (Rainfall)
TM1 Temp Sensor
SM1 Soil Moisture Sensor
Nulls (Others)
Measurement Type
Meteorological Attribute
8 types
Measurement_Type
Wind Direction
Relative Humidity
Differential Pressure
Differential Pressure
Wind Speed
Wind Speed
Temperature
Temperature
Cumulative Precipitation
Cumulative Precipitation
Temperature
Soil Moisture
TimeWindowBoundary
Soil Moisture

## Slide 7
Measurement Medium
Data Overview
Atmosphere, Soil
When it is not MK-III, Sensor, we have Nulls
Measurement Time
All Argyle stations except for bioswale have a start date of 13/03/2017 and end date as 16/04/2018
Argyle bioswale station have start date of 10/03/2017 and end date of 16/04/2018.
All Langley stations have a start date of 19/03/2017.
All Langley stations except for sensor and bioswale have end date of 04/01/2018 and for the exceptions it is 16/04/2018
All UI lab stations except for NWS precipitations have a start date of 19/03/2017
For NWS precipitations data collection started on 27/04/2017
UI labs data collection ended on 12/04/2018, 25/04/2018, 03/05/2018, 04/05/2018

## Slide 8
Measurement Value
Measurement Title | Units | Count | Min_Value | Max_Value | Avg_Value
UI Labs Bioswale - Thunder 1: MK-III Weather Station Wind Direction | deg from North | 338454 | 0 | 360 | 203.56
Langley - Thunder 1: MK-III Weather Station Wind Direction |  | 162006 | 0 | 360 | 96.08
Argyle - Thunder 1: MK-III Weather Station Wind Direction |  | 496449 | 0 | 360 | 168.47
UI Labs Bioswale - Thunder 1: MK-III Weather Station RH | percent (%) | 337788 | 0 | 100 | 67.66
Langley - Thunder 1: MK-III Weather Station RH |  | 162019 | 0 | 99 | 31.54
Argyle - Thunder 1: MK-III Weather Station RH |  | 496458 | -1 | 100 | 35.96
UI Labs Bioswale - Thunder 1: MK-III Weather Station Pressure | pascals (Pa) | 338652 | 0 | 10155 | 9932.81
Langley - Thunder 1: MK-III Weather Station Pressure |  | 162021 | 0 | 10205 | 4637.67
Argyle - Thunder 1: MK-III Weather Station Pressure |  | 496457 | 0 | 10221 | 9977.37
UI Labs Bioswale - Cumulus: Weather Station Pressure | pascals (Pa) | 342184 | 0 | 101550 | 99323.46
Langley - Cumulus: Weather Station Pressure |  | 164256 | 0 | 102050 | 45112.54
Argyle - Cumulus: Weather Station Pressure |  | 425691 | 0 | 102210 | 99812.08
UI Labs Bioswale - Thunder 1: MK-III Weather Station Wind Speed | meters per second (m/s) | 338546 | 0 | 122 | 10.67
Langley - Thunder 1: MK-III Weather Station Wind Speed |  | 162007 | 0 | 129 | 7.61
Argyle - Thunder 1: MK-III Weather Station Wind Speed |  | 496452 | 0 | 103 | 4.86
UI Labs Bioswale - Cumulus: Weather Station Wind Speed | meters per second (m/s) | 342091 | 0 | 12.2 | 1.01
Langley - Cumulus: Weather Station Wind Speed |  | 164278 | 0 | 12.9 | 0.74
Argyle - Cumulus: Weather Station Wind Speed |  | 425690 | 0 | 10.3 | 0.36
UI Labs Bioswale - Thunder 1: MK-III Weather Station Temp | deg celsius (degC) | 338908 | -63 | 65535 | 355.70
Langley - Thunder 1: MK-III Weather Station Temp |  | 161999 | -225 | 177 | -0.55
Argyle - Thunder 1: MK-III Weather Station Temp |  | 496464 | -550 | 65535 | 361.53
UI Labs Bioswale - Cumulus: Weather Station Air Temp | deg celsius (degC) | 342474 | -6.3 | 6553 | 35.28
Langley - Cumulus: Weather Station Air Temp |  | 164262 | -22.5 | 17.7 | 0.00
Argyle - Cumulus: Weather Station Air Temp |  | 425689 | -55 | 6553 | 38.54
UI Labs Bioswale - Thunder 1: MK-III Weather Station Rainfall | count | 338373 | 0 | 5962 | 3360.62
Langley - Thunder 1: MK-III Weather Station Rainfall |  | 161963 | 0 | 199 | 76.14
Argyle - Thunder 1: MK-III Weather Station Rainfall |  | 496451 | 0 | 4047 | 1388.16
Langley - Cumulus: Weather Station Rainfall | Inches (In) | 164310 | 0 | 1.99 | 0.74
Argyle - Cumulus: Weather Station Rainfall |  | 425688 | 0 | 40.47 | 12.43
UI Labs Bioswale - Thunder 1: TM1 Temp Sensor | milliVolts (mV) | 553058 | 199 | 611 | 443.03
Langley - Thunder 1: TM1 Temp Sensor |  | 528093 | 217 | 540 | 383.02
Argyle - Thunder 1: TM1 Temp Sensor |  | 520707 | 0 | 3301 | 3293.77
UI Labs Bioswale - Thunder 1: SM1 Soil Moisture Sensor | milliVolts (mV) | 553057 | 705 | 1088 | 940.58
Langley - Thunder 1: SM1 Soil Moisture Sensor |  | 528082 | 675 | 990 | 832.13
Argyle - Thunder 1: SM1 Soil Moisture Sensor |  | 520706 | 0 | 1208 | 612.18
UI Labs Bioswale NWS Quantitative Precipitation Forecast | Universal Coordinated time (UTC) | 1492 | 0 | 1.81 | 0.03
UI Labs Bioswale NWS Probability of Precipitation |  | 745 | 0 | 100 | 26.30
Langley - Cumulus: Bioswale Calibrated VWC | Percent Volumetric Water Content (%(vwc)) | 529160 | 15.036 | 36 | 25.51
Argyle - Cumulus: Bioswale Calibrated VWC |  | 196519 | -16.79424 | 64.3408 | 37.29

## Slide 9
Learnings
When Accessing S3 with databricks, its always preferrable to use them with same region.
We can try and use Atmospheric conditions to predict ground water level
Comparison of cluster profiles w.r.t Indian data Sets. (Obviously not)
Differences between weather stations and their collection w.r.t long range and normal
https://w1.weather.gov/data/obhistory/KORD.html
https://www.isws.illinois.edu/statecli/general/chicago-climate-narrative.htm

## Slide 10
Colab notebook
Data Dictionary
Distributions
Motivation.
Iot data simulation